RULES

2 and 4 Wheel Drive Street Stock Trucks

The Street Stock class is designed for daily driven, on the road pickup trucks (full bodied diesel pickup trucks). Must have factory bed, no flatbeds, wreckers, etc.

Valid driver’s licenses, DOT registration and license plates and insurance are mandatory.

No four-wheel drive vehicles.

Weight limit: 8500 lbs. weight is with driver, and passenger if one.

No added weight, truck may have empty bed mounted aluminum tool box.

The batteries must have securely mounted in stock location.

Body: The body must be the OEM truck body, including the full bed floor. The body must retain full sheet metal. Metal aftermarket hoods are permitted. Fiberglass is prohibited. The hood must be closed and securely latched while the vehicle is hooked to the sled. The complete OEM firewall and OEM floor plan is mandatory.

Bumpers: Truck must have Factory front and rear bumpers, no aftermarket bumpers.

Brakes: Four-wheel hydraulic brakes are mandatory.

Chassis: The OEM chassis is mandatory. The engine must be in the OEM location for the body used. The vehicle must retain the full OEM chassis. Wheel tubs, back-half conversions, tube chassis, etc. are prohibited.

Cooling System: Radiators must be in the stock location and be of at least stock size.

Driveline: An OEM transmission and transfer case are mandatory.

Driver Restraint System: The OEM restraining system is mandatory and must be worn.

Engine: The engine is limited to a stock. OEM make-specific compression ignition engine. NITROUS OXIDE is prohibited along with other oxygen extenders as well.